RADVOP – Efficient radar forward operator for data assimilation and model verification
Ulrich Blahak2, Yuefei Zeng1, Dorit Epperlein1, Daniel Leuenberger3
1Institute for Meteorology and Climate Research,
Karlsruhe Institute of Technology (KIT)
2German Weather Service
3MeteoSwiss
EMF Jahrestreffen, 5.4.2013

---
Characteristics
- Develop efficient radar forward operator suitable for:
  - Ensemble based radar data assimilation (LETKF)
  - Model microphysics verification
  - Radial wind, reflectivity, if time allows some polarization parameters
- Code offers, in a modular and configurable fashion, different levels of complexity for different physical processes (beam propagation, backscattering, extinction, etc.). This enables to determine the setup with the „best“ compromise between numerical costs and physical accuracy for different applications.
- Forward operator online coupled to the COSMO-model, parallel and vectorizable code, easy to use framework. Coupling to other models possible but requires some work.
- Honors all COSMO-model microphysics schemes including the Seifert-Beheng 2-moment scheme

---
Block diagram of the operator
(red: not implemented yet!)

---
Options for Ze and attenuation
Mie-scattering (one- or two-layered spheres):
   → Integration of σback and σext over N(D):
       σback = f(D,m) , m = refract. index hydrometeors (ice/water/air-mixtures, different possibilities)
       σext = f(D,m) (itype_refl = 1; lext_dbz = .true.)
Rayleigh approx. (no attenuation!): σback ~ D6 (itype_refl = 2)
    → water drops: Ze ~ M6 (analytic for gamma size distr.)
    → solid hydrom.: m variable, still need to integrate over N(D)
Rayleigh + Debye approximation for m: (itype_refl = 3)
   → water drops: Ze ~ M6
    → solid hydrom.: Ze ~ ρ2bulk(D) M6

---
Obs Sim. simple
Obs Sim. simple
Results for different configurations in a real case (30.6.2012, Fürholzen)
Ze
vr
+ SODE + beam function (online beam prop.) + Refl. weighting
+ SODE + beam function (online beam prop.) + Refl. weighting
+ Mie + attenuation
+ Mie + attenuation

---
Case studies with all German radars
Simulation COSMO-DE Ze Obs
Overlay of lowest elevations (in overlap regions: values from lowest height).
Echoes mostly from the rain region.

---
COSMO-DE model verification - CFADs
Simulation Ze Obs
Lowest elevation, echoes mostly from the rain region:
model overestimates Z
CFAD of Z of all elev.:
  too broad distr. in the model
  below melting level:
      in the model some very high Z-values present
  above:melting level: Z too low

---
Summary and Status
- Radar forward operator nearly finished w.r.t. radial wind and reflectivity.
- Parallel online coupled version for COSMO-model and serial offline version (Fortran2003)
- Can simulate several radars in parallel. These can have different scan strategies and radar wavelengths (most efficient if all radars have same wavelength). Scan strategies at the moment limited to azimutal volumne scans of arbitrary elevations, azimut- and range-intervals. RHIs and vertically pointing mode possible but not implemented yet. For simplicity and efficiency, all data of the volume scan are obtained at the same time (time stamp of radar data) instead of at their true measuring time.
- Operator namelist driven; radar meta data from namelist or directly from obs data files
- Have demonstrated applicability for:
  - Model verification, e.g., by CFADs
  - KENDA LETKF ensemble data assimilation!
- Have demonstrated good efficiency on the NEC SX9
  (except for file I/O ...)
- Remaining work:
  - RHIs, vertically pointing mode, „true-time/true-location“ mode
  - Polarisation parameters based on SYNPOLRAD of DLR or other existing T-matrix code
  - Asynchoneous parallelization mode for massive parallel systems
  - ...

---
Example: COSMO-DE, RADVOP online
COSMO-DE 4.9.2011
15 UTC run, radars every 5 min, full volume scans
16 radars, most simple operator config (Rayleigh, offline-beam prop., no pulse volume averaging)
Computed on NEC-SX9, operator caused model runtime increase < 10 %
simple overlay of PPIs from the 1,5° elevation